## Slide 1: Micromobility Especially in Germany
Dipl.-Ing. Sven Lißner
2021
Faculty of Transport and Traffic Sciences – Chair of Transport Ecology
Prof. Dr.-Ing. Udo Becker

## Slide 2: Content and learning objectives
Content:
What is micromobility?
Which forms exist?
Environmental impacts of micromobility
Safety aspects
Learning objectives:
To get to know micromobility
Know and classify impacts

## Slide 3: What is micromobility?
This term covers short-distance mobility concepts, usually the first and last "mile" of a trip. According to a study by the McKinsey Center for Future Mobility, about 60 per cent of car trips worldwide involve a distance of less than eight kilometres, making these trips eligible for micromobility solutions. [McKinsey, 2019]
So 0-8 km distance is micromobility, the mode doesn't matter?
Micromobility is the term for electrically powered micro-vehicles. These mainly electric vehicles are used as an alternative to the usual means of transport. [Mobilität365, 2019]
So you mean electric vehicles?
There is probably no universally valid definition yet.
Rather a cloud of possible interpretations of the word micromobility

## Slide 4: What is micromobility? – We try to find our own definition.
Mobility characterises the enabling of necessary changes of location to satisfy needs.
So: What possibilities are there for me to get from point A to point B?
This can be done directly: door-to-door by car, but politically this is less desired.
Alternatively, of course, the bicycle can also be used.

## Slide 5: What is micromobility?
If you use public transport, the route almost inevitably becomes a chain of routes.
In many cases, the location of bus stops results in access and departure routes.
These routes are usually quite short (last mile).
In some cases, however, they are not short enough to walk.
Therefore, a mean of transport for short access and departure routes fulfils per se the definition of micromobility.
?
?

## Slide 6: What is micromobility?
So, if we want to strengthen public transport, we need minimal discomfort along the route chain!
Micromobility offers can help in the pre- and post-commute.
What the user needs:
  Flexibility
  Reliability
  Reasonable prices
  Easy booking
Source: DVB AG
Source: Tier Mobility GmbH

## Slide 7: What is micromobility?
Which means of transport can be used for this?
Source:
dpa
Source: Constantin Müller
Source: Verena Engel
Source: Dirk Schmidt
E-scooter
E-bikes
Sharing-bikes
Skateboards
Monowheels
Hoverboards
Others
Source: Microsoft

## Slide 8: What is micromobility?
Who are the actors?
private individuals owning and, if necessary, carrying scooters bicycles etc. large variety of individual solutions | transport operators offer bike-sharing services in the transport association | private business offer sharing services (bike, scooter, e-scooter) part of MaaS concepts
Cities? - Indirectly, too!

## Slide 9: What is micromobility?
Commissions operation, sells service to end customer
operates public transport via municipal enterprise or commissions enterprise
specifies restricted areas and areas of use
Bike sharing service and operation
Services of General Interest
Voluntary commitment for supply quality

## Slide 10: What have we learned so far?
Micromobility wants to be used primarily in route chains.
It offers itself as a solution for the last mile.
It is small!
It is often electric (but does not have to be).
It can be organised privately, commercially and (partly) publicly.

## Slide 11: What is micromobility?
Why are we doing this lecture?
In Germany, there are two triggers: 1. The bikesharing boom in 2016:

## Slide 12: What is micromobility?
Why are we doing this lecture?
In Germany, there are two triggers: 2. The e-scooter boom driven by the small electric vehicles regulation 2019

## Slide 13: Small electric vehicles regulation
§ 1 Scope of application
For the purposes of this ordinance, micro electric vehicles are motor vehicles with electric propulsion and a maximum design speed of not less than 6 km/h and not more than 20 km/h, which have the following characteristics
vehicle without seat or self-balancing vehicle with or without seat,
a steering or grab bar of at least 500 mm for motor vehicles with a seat and of at least 700 mm for motor vehicles without a seat,
a rated continuous output of not more than 500 watts, or of not more than 1400 watts if at least 60 per cent of the output is used for self-balancing[...],
an overall width of not more than 700 mm, an overall height of not more than 1400 mm and an overall length of not more than 2000 mm; and
a maximum vehicle mass without driver of not more than 55 kg.

## Slide 14: Small electric vehicles regulation
§ 2 Commissioning requirements
A small electric vehicle may only be put into operation on public roads if
it corresponds to a type for which a general type-approval has been granted or an individual type-approval has been granted for the vehicle,
it carries a valid insurance sticker for very small electric vehicles in accordance with § 29a of the Vehicle Registration Ordinance,
it [...] is marked with a vehicle identification number and a manufacturer's plate with the following specifications:
  the vehicle type must be indicated on the factory plate as “small electric vehicle",
  [...] the maximum design speed and the approval number of the general type-approval or individual type-approval for the vehicle shall be indicated on the factory plate, and
It meets
  the requirements for the deceleration device according to § 4,
  the requirements for the lighting equipment according to § 5 paragraph 1 sentence 1 and paragraph 3,
  the requirements for the device for acoustic signals according to § 6 sentence 1 as well as
  the other safety requirements according to § 7.

## Slide 15: Small electric vehicles regulation
Must ride on the cycle path, even if it is not obligatory to use!
Must not be moved on the footpath even when switched off.
If there is no cycle path, the road may be used.
Insurance is compulsory.
The 0.5 ‰ blood alcohol limit applies. Except for new drivers and people under 21 years (0.0‰).
No one is allowed to be carried! Also no objects on the running board!

## Slide 16: Small electric vehicles regulation
So the idea is that a new mobility offer is given a legal framework!
But how does this work in practice?
        Distribution is a problem.
        Vehicles block footpaths.
        In pedestrian zones, the ban is often ignored!
        There are conflicts of use with pedestrians.
        And cyclists are often not happy about 20 km/h obstacles either.
Source: Clemens Rath
Source: Philipp Böhme

## Slide 17: Small electric vehicles regulation
Around 50% of respondents feel that the scooters are annoying.
Just under 40% accept e-scooters!
“Disruptive”
Almost half of Germans want to get rid of e-scooters
They block sidewalks, disturb pedestrians and cause accidents. Germans have not yet become accustomed to using e-scooters. This is also shown by a representative survey.

## Slide 18: Who offers micromobility?

## Slide 19: Sharing provider
Which providers are there in Germany?
11.600 scooters at 9 locations (09/2019)
In 2021: 57 locations
32.000 scooters at 12 locations (09/2019) In 2021: 16 locations
11.500 scooters at 7 locations (09/2019)
??? scooters at 5 locations (09/2019) In 2021: 28 locations
Source: Lime, TIER, voi, Bird

## Slide 20: Sharing provider
Number of e-scooters in German cities by provider (09/2019)
Source: Statista, 2020

## Slide 21: Sharing provider - bicycles
Status 2020
Status 2018

## Slide 22: Sharing provider - bicycles
Status 2020 - Germany
63 cities station-bound also e-bikes | 3 cities free-floating no e-bikes | 43 cities station-bound no e-bikes | 7 cities free-floating low e-bike share | 2 cities free-floating e-bikes

## Slide 23: Sharing provider - bicycles
Bicycles and e-bikes are becoming a throwaway resource in the battle for market share!
Source: velobiz.de, 2020
Source: theatlantic.com, 2019

## Slide 24: Sharing provider – company bike
Since 2012, company bicycles for private use have been treated the same as cars (1% regulation).
Since 2019, the 0.5% rule has applied (in the course of the improved status of e-cars).
Since 2020, only 0.25% of the imputed income has been taxed.
How does it work?
The employer must participate in a service bike programme.
The employee chooses a bicycle and leases it for 3 years.
The employer pays the leasing fees and deducts them from the employee's gross salary.
0.25% of the list price is taxed as imputed income.
The employee has a new bicycle and, due to the reduced tax burden, almost no costs.
After 3 years, the employee can decide whether to return the bike or to buy it at a favourable final instalment.

## Slide 25: Sharing provider – company bike
In 2019, 220,000 bicycles were already leased.
In 2020, 350,000 bikes are already forecast. A total of approx. 700,000 leased bikes on the road.
Mostly high-priced bikes are leased (according to IBK, most bikes cost over €2,500).
80% - 90% e-bikes!
There are still no statistics on use! (i.e. whether the bikes are actually used instead of cars)
There are already secondary recyclers who take care of returns (but there are only a few returns).

## Slide 26: How are micromobility services used?
Sources: Philipp Böhme, Constantin Müller

## Slide 27: E-scooter
Age distribution of e-scooter users in Portland (Source: PBoT, 2019)
Age distribution e-scooter users Paris (Source: 6t –buereau de recherche, 2019)
Age distribution
Age
Share in percent
Their Age:
Quantity
Younger than 25 years
years
years
years
years
Total
years and older
Mean value

## Slide 28: E-scooter
E-scooter user frequency Portland (Source: PBoT, 2019)
E-scooter user frequency Paris (Source: 6t –buereau de recherche, 2019)
(almost) daily
2-3 times a week
once a week
1-3 times a month
less
once
In total
User frequency Paris
User frequency Portland
once

## Slide 29: E-Scooter
Alternative mode of transport Portland (Source: PBoT, 2019)
Alternative mode of transport Paris (Source: 6t –buereau de recherche, 2019)
Chart: Used instead of e-scooters:
| Fuß | Uber | Eigener Pkw | ÖPNV | kein Weg | eigenes Fahrrad | Leihfahrrad | sonstiges
Portland | 0.36 | 0.2 | 0.18 | 0.09 | 0.07 | 0.04 | 0.04 | 0.02
Paris | 0.47 | 0.04 | 0.03 | 0.29 | 0.03 | 0.02 | 0.07 | 0.05
others
bike sharing
own bike
no trip
Public transport
own car
Uber
walking

## Slide 30: E-Scooter in Dresden (Germany)
Age distribution
Share in percent
Age
65% male
55% touristic use
33% out of curiosity
pupils
students
trainees
unemployed
others
employees/ self-employed
Employment
Share in percent
Source: von Rechenberg, 2020

## Slide 31: E-Scooter in Dresden (Germany)
User frequency
Purpose of route
Source: von Rechenberg, 2020

## Slide 32: E-scooter in Dresden (Germany)
87% of the respondents said that their choice of transport had not changed!
7% said they used the car slightly less.
5% said they used public transport more often.
walking
cycling
bike sahring
own car
Car sharing
taxi
public transport
no trip
pedal scooter
Which transport mode was replaced?
Replaced transport mode
Share in percentage
Source: von Rechenberg, 2020

## Slide 33: E-scooter in Dresden (Germany)
Daily pattern shows peaks in the afternoon and evening.
In addition, increased use at weekends.
1120 trips per day in the city = 1.85 trips per scooter per day.
Average utilisation of 50% => half of the scooters were not used.
Source: Poroijkow, 2020

## Slide 34: Bike sharing in Copenhagen (Denmark)
Source: von Harten, 2020

## Slide 35: Bike sharing in Copenhagen (Denmark)
Source: von Harten, 2020

## Slide 36: Bike sharing in Copenhagen (Denmark)
Source: Poroijkow, 2020

## Slide 37: Bike sharing in Copenhagen (Denmark)
Source: von Harten, 2020

## Slide 38: Other data available
So far, there are no statistics on other micromobility services.
However, their role is currently still very limited.
There are also no further statistics on bicycle leasing.
Unfortunately, this means that these offers cannot be evaluated yet.

## Slide 39: Results of a life cycle assessment of micromobility
Sources: Philipp Böhme, Constantin Müller

## Slide 40: Input data for the life cycle assessment
We attempt a life cycle analysis according to the DIN EN ISO 14040.
Principle Well - to – Wheel, so the complete life cycle is considered.

## Slide 41: Life cycle inventory of an e-scooter
Chart: 
| Aluminiumrahmen | Stahlteile | Li-ion Akku | Elektromotor | Reifen und Schläuche | Ladegerät | LED´s | Plastik | Pulverbeschichtung | Leiterplatten | Verdrahtung
 | 50.2 | 11.7 | 10 | 10 | 6.9 | 1.8 | 1.8 | 1.8 | 1.8 | 1.8 | 1.8
Source: Lißner, 2020

## Slide 42: Life cycle inventory of an e-scooter
Chart: Charger
| Aluminium | Ferrite | Kupfer | Stahl | Leiterplatten | Kondensator | Kunststoffe | Messing | Keramik
 | 49.8 | 12.1 | 11.7 | 8.4 | 6.9 | 5.5 | 3.9 | 1.8 | 0.1
Chart: Electric motor
| Eisen | Aluminium | Kupfer | Polyethylen
 | 58 | 20 | 20 | 2
iron
aluminium
copper
polyethylene
aluminium
ferrites
copper
steel
circuit boards
condenser
plastics
brass
ceramics
Source: Lißner, 2020

## Slide 43: Life cycle inventory of an e-scooter
Calculation of environmental impacts of the production of e-scooters |  |  |  |  |  |  | 
Component | Mass Lime Scooter in g | Lime CO2 equivalent in kg | Lime SO2 equivalent in kg | Lime TOPP equivalent in kg | Lime PO4 in kg | Lime NOX in kg | Lime PM10 in kg
Aluminum frame | 11,550 | 138,600 | 0,508 | 0,455 | 0,033 | 0,236 | 0,274
Steel parts | 2,700 | 4,050 | 0,011 | 0,018 | 0,001 | 0,009 | 0,005
Li-ion (NMC111) battery | 2,310 | 14,361 | 0,213 | 0,004 | 0,012 | 0,066 | 0,002
Electric motor | 2,310 | 7,779 | 0,036 | 0,028 | 0,002 | 0,016 | 0,000
Tires and tubes | 1,600 | 5,248 | 0,018 | 0,026 | 0,002 | 0,013 | 0,002
Charger | 0,420 | 2,923 | 0,013 | 0,010 | 0,001 | 0,677 | 0,000
LEDs | 0,420 |  |  |  |  |  | 
Plastic | 0,420 | 1,096 | 0,003 | 0,007 | 0,000 | 0,003 | 0,000
Powder coating | 0,420 |  |  |  |  |  | 
Circuit boards | 0,420 | 1,764 | 0,013 | 0,007 | 0,001 | 0,005 | 0,003
Cabling | 0,420 | 1,764 | 0,012 | 0,007 | 0,001 | 0,005 | 0,003
Sum | 22,990 | 177,59 | 0,827 | 0,56 | 0,053 | 1,031 | 0,289

## Slide 44: Life cycle inventory of an e-scooter
Calculation of environmental impacts of the production of the charger |  |  |  |  |  |  |  | 
Charger | Mass in kg | CO2 equivalent in kg | SO2 equivalent in kg | TOPP equivalent in kg | PO4 in kg | NOX in kg | Dust in kg | %
Overall device | 0,420 | 2,923 | 0,013 | 0,010 | 0,001 | 0,677 | 0,236 | 100
Aluminum | 0,209 | 2,510 | 0,009 | 0,008 | 0,001 | 0,001 | 0,005 | 49,8
Iron | 0,051 | 0,007 | 0,000 | 0,000 | 0,000 | 0,000 | 0,000 | 12,1
Copper | 0,049 | 0,206 | 0,001 | 0,001 | 0,000 | 0,074 | 0,000 | 11,7
Steel | 0,035 | 0,053 | 0,000 | 0,000 | 0,000 | 0,004 | 0,000 | 8,4
Circuit boards | 0,029 | 0,122 | 0,001 | 0,000 | 0,000 | 0,333 | 0,231 | 6,9
Capacitor | 0,023 | 0,010 | 0,000 | 0,000 | 0,000 | 0,266 | 0,000 | 5,5
Plasticy | 0,016 | 0,000 | 0,000 | 0,000 | 0,000 | 0,000 | 0,000 | 3,9
Brass | 0,007 | 0,015 | 0,001 | 0,000 | 0,000 | 0,000 | 0,000 | 1,6
Ceramics | 0,000 | 0,000 | 0,000 | 0,000 | 0,000 | 0,000 | 0,000 | 0,1
Calculation of environmental impacts of the production of the electric motor |  |  |  |  |  |  |  | 
Electric motor | Mass in kg | CO2 equivalent in kg | SO2 equivalent in kg | TOPP equivalent in kg | PO4 in kg | NOX in kg | Dust in kg | %
Overall device | 2,310 | 7,779 | 0,036 | 0,028 | 0,002 | 0,016 | 0,015 | 100
Iron | 1,340 | 0,174 | 0,002 | 0,002 | 0,000 | 0,001 | 0,000 | 58
Aluminum | 0,462 | 5,544 | 0,020 | 0,018 | 0,001 | 0,009 | 0,011 | 20
Copper | 0,462 | 1,940 | 0,014 | 0,007 | 0,001 | 0,005 | 0,004 | 20
Polyethylene | 0,046 | 0,121 | 0,000 | 0,001 | 0,000 | 0,000 | 0,000 | 2

## Slide 45: Life cycle assessment of an e-scooter
Raw data calculation of environmental impacts |  |  |  |  |  |  | 
Product | CO2 equivalent in kg | SO2 equivalent in kg | TOPP equivalent in g | NOX in g | PM10 in g | NH3 | PO4
1 kg aluminium_De_2020 | 12000,00 | 44,00 | 39,40 | 20,40 | 23,70 | 0,612 | 2,854
1 kg metal_steel_mix_De_2020 | 1500,00 | 4,09 | 6,79 | 3,50 | 1,76 | -0,008 | 0,452
1 kg li-ion (NMC111) battery | 6216,76 | 92,22 | 1,79 | 28,71 | 0,71 | 4,626 | 5,259
1 kg Chem-OrgGummi-DE2000 | 3280,00 | 11,00 | 16,00 | 8,15 | 1,06 | 0,003 | 1,061
1 kg wire_copper_circuit board | 4200,00 | 30,00 | 15,50 | 11,50 | 7,96 | 0,044 | 1,510
1 kg wire_copper_wiring | 4200,00 | 29,00 | 15,50 | 11,50 | 7,96 | 0,044 | 1,510
1 kg MetalFe_Pellets_Import_mix_De_2020 | 130,00 | 1,48 | 1,35 | 1,02 | 0,12 | 0,000 | 0,133
1 kg_LDPE_2020_De_Polyethylen | 2610,00 | 7,03 | 16,70 | 7,93 | 0,54 | 0,000 | 1,031
Plastics | 1,91 | 0,00 | 0,01 | 0,00 | 0,51 | 0,048 | 0,016
Brass | 2297,00 | 100,00 | 0,14 | 19,90 | 14,30 | 2,57 | 3,4351
1 kg stones_soils_ceramics | 602,00 | 1,44 | 1,84 | 1,36 | 0,11 | 0,000 | 0,177

## Slide 46: Life cycle assessment of an e-scooter: Transport
Transport via cargo ship or air freight.
From Shanghai to Bremerhaven.
Further distribution by truck.
Transhipment operations and packaging not included!
Source: CMA CGM
Source: Cekay
Source: Wikimedia Commons

## Slide 47: Life cycle assessment of an e-scooter: The use
Emission factor for electricity mix in Germany 2019 = 401g/CO2 per KWh
Electricity consumption e-scooter per km: 0.01kwh/km
CO2 emissions per km: 5g
Additionally, charging losses have to be considered (20%)

## Slide 48: Life cycle assessment of an e-scooter: The use
Total consumption and emissions over the use phase Ford Transit |  |  | 
Lifespan in days | km | Consumption in l | TotalCO2 emissions in g
28 | 0,965 | 3,352 | 8.866,234
28 | 3,701 | 12,849 | 33.987,229
28 | 6,436 | 22,346 | 59.108,224
540 | 0,965 | 64,643 | 170.991,648
540 | 3,701 | 247,799 | 655.467,984
540 | 6,436 | 430,955 | 1.139.944,320
730 | 0,965 | 87,388 | 231.155,376
730 | 3,701 | 334,987 | 886.095,608
730 | 6,436 | 582,587 | 1.541.035,840
Redistribution, maintenance and charging.
Assumption about the distances travelled by vans from own surveys and international studies.
Calculated over the service life.
Source: imago images

## Slide 49: Life cycle assessment of an e-scooter: The overall balance
szenario | life-span | transport | trips per day | trip lenght per day | collection | driving perfor-mance |  |  |  |  |  |  | Co2 eq | So2 eq | TOPP eq | NOX | PM10
 | day | type | number | km | factor | km | CO2 (of production) | CO2 (production) per km | transport | collection | usage | check sum | g/pkm |  |  |  | 
1 | 28 | Sea vessel/ truck | 1 | 1,82 | 0,2 | 51,0 | 177.585,0 | 3.484,8 | 34,56 | 25,68 | 4,95 | 3.550,0 | 3.524,33 | 16,23 | 11,02 | 1,05 | 20,24
2 | 28 | Sea vessel/ truck | 4,6 | 1,88 | 0,2 | 242,1 | 177585,0 | 733,4 | 7,27 | 5,40 | 4,95 | 751,0 | 745,62 | 3,42 | 2,33 | 0,22 | 4,26
3 | 28 | Sea vessel/ truck | 6,6 | 1,93 | 0,2 | 356,7 | 177585,0 | 497,9 | 4,94 | 3,67 | 4,95 | 511,5 | 507,80 | 2,33 | 1,58 | 0,15 | 2,89
4 | 90 | Sea vessel/ truck | 1 | 1,82 | 0,2 | 163,8 | 177585,0 | 1.084,2 | 10,75 | 7,99 | 4,95 | 1.107,9 | 1.099,87 | 5,06 | 3,43 | 0,32 | 6,30
5 | 90 | Sea vessel/ truck | 4,6 | 1,88 | 0,2 | 778,3 | 177585,0 | 228,2 | 2,26 | 1,68 | 4,95 | 237,1 | 235,38 | 1,07 | 0,73 | 0,07 | 1,33
6 | 90 | Sea vessel/ truck | 6,6 | 1,93 | 0,1 | 1.146,4 | 177585,0 | 154,9 | 1,54 | 0,57 | 4,95 | 162,0 | 161,39 | 0,73 | 0,50 | 0,05 | 0,90
7 | 180 | Sea vessel/ truck | 1 | 1,82 | 0,2 | 327,6 | 177585,0 | 542,1 | 5,38 | 3,99 | 4,95 | 556,4 | 552,41 | 2,53 | 1,72 | 0,16 | 3,15
8 | 180 | Sea vessel/ truck | 4,6 | 1,88 | 0,2 | 1.556,6 | 177585,0 | 114,1 | 1,13 | 0,84 | 4,95 | 121,0 | 120,17 | 0,54 | 0,37 | 0,03 | 0,66
9 | 180 | Sea vessel/ truck | 6,6 | 1,93 | 0,1 | 2.292,8 | 177585,0 | 77,5 | 0,77 | 0,29 | 4,95 | 83,5 | 83,17 | 0,37 | 0,25 | 0,02 | 0,45
10 | 360 | Sea vessel/ truck | 1 | 1,82 | 0,2 | 655,2 | 177585,0 | 271,0 | 2,69 | 2,00 | 4,95 | 280,7 | 278,68 | 1,27 | 0,86 | 0,08 | 1,57
11 | 360 | Sea vessel/ truck | 4,6 | 1,88 | 0,2 | 3.113,3 | 177585,0 | 57,0 | 0,57 | 0,42 | 4,95 | 63,0 | 62,56 | 0,27 | 0,19 | 0,02 | 0,33
12 | 360 | Sea vessel/ truck | 6,6 | 1,93 | 0,1 | 4.585,7 | 177585,0 | 38,7 | 0,38 | 0,14 | 4,95 | 44,2 | 44,06 | 0,19 | 0,13 | 0,01 | 0,22

## Slide 50: Life cycle assessment of an e-scooter: The overall balance
Chart: E-scooter CO2 equivalent emissions in g per pkm
| 51 | 164 | 242 | 328 | 357 | 655 | 778 | Pkw | 1146 | 1557 | 2293 | 3113 | 4586
 | 3490.8436 | 1089.4523 | 738.5701 | 547.2026 | 503.0155 | 276.0778 | 233.1894 | 185 | 159.9052 | 119.0712 | 82.4291 | 62.0121 | 43.691
car
Source: Lißner, 2020

## Slide 51: Evaluation of the life cycle assessment
Under current conditions, e-scooters are in some cases much worse than cars in terms of their CO2 balance.
Lifecycle is too short (vandalism).
Usage rate is too low (price!).
In the sharing model, a significant improvement currently appears difficult.
The same applies to e-bike sharing. However, the distances are longer and the lifetimes longer!

## Slide 52: Safety of micromobility
Sources: Philipp Böhme, Constantin Müller

## Slide 53: Road safety aspects
Study from Tempe, Arizona (Sanders, 2019)
Safety concerns regarding injury to others,
or inadequately safe traffic space,
or fitness to drive.

## Slide 54: Conclusion
Sources: Philipp Böhme, Constantin Müller

## Slide 55: Conclusion
Properly used, micromobility is a useful complement to public transport.
However, usage patterns do not currently indicate that a desired modal shift is taking place!
Instead, there is a lot of undesired modal shift from environmental transport.
The organisational form is not yet coherent. Many things are possible, but currently with many undesirable side-effects.
Cities are currently rather driven and do not act with their own clear plan.

## Slide 56: Micromobility Especially in Germany
Dipl.-Ing. Sven Lißner
2021
Faculty of Transport and Traffic Sciences – Chair of Transport Ecology
Prof. Dr.-Ing. Udo Becker
Grant Agreement No.:
2019-1-PL01-K1203-065244